VVL tech notes

Two methods for digital recording with the current workstation:

1) Current procedure involves recording in real time through the sound card's utility software.

Advantages:  Is fastest mode of capture.  Data is written to server as it streams off of tape.

Is simple and easy for operator.  Operator can focus on note taking.

Disadvantages:  Lacks quality control or integrity checks at capture stage.

Needs uninterrupted access to the network and server to avoid corrupted files.

No wav header access which would allow for embedding of metadata.

Carries some risk of overwriting old files by mistake.  Fail-safe measures must

be in place.

2.) Optional approach involves the use of audio editing software to record tapes, such as Cool Edit.

Advantages:  Gives operator an extra interface to monitor recorded sound file properties such

as levels and clipping.

Adds a first pass at some quality control.  Can view the envelope or listen to the file and check for problems.

Provides instant access to the wav header where metadata can be embedded and saved with file

Saves time at the segmentation stage - metadata already entered into header*

Disadvantages:  Not as simple.  Involves more steps including a final "save" which adds time.

Cuts down productivity an average of up to 30 minutes per tape or 5 - 10 minutes per band at the capture stage (*some of this time may be made up for at the segmentation stage - see advantages above)

R. Peiffer

9/24/99